## Slide 1
Atmosphere
Measurement
Stellar
Surface
Spectroscopy
Scatter
CIA
First layer of code: Reading inputs and defining retrieval procedure
Input files
NEMESIS Python classes
Optimal Estimation
Nested sampling
Layer
Output files
NEMESIS Python classes
Variables

## Slide 2
Atmosphere
Atmosphere.NVMR : Number of gases in reference atmosphere
Atmosphere.IPLANET : Planet ID number
Atmosphere.ID(NVMR) : Radtran ID of each gas
Atmosphere.ISO(NVMR) : Radtran Isotopologue ID of each gas
Atmosphere.AMFORM: Flag indicating how the molecular weight has to be computed
………………………………………………………….
Parameters and attributes
Methods
Atmosphere.calc_grav() : Based on the Planet ID, it calculates the gravity field at each altitude
Atmosphere.calc_molwt() : Based on AMFORM, it calculates the molecular weight at each altitude
Atmosphere.hydrostatP() and Atmosphere.hydrostatH() : Recomputes altitudes or pressure levels based on hydrostatic equilibrium
Atmosphere.adjust_VMR() : If needed, it re-scales the VMR of each gas for all of them to add up to 1.0
Atmosphere.read_ref() : Reads .ref file to fill the parameters and attributes of this class

## Slide 3
Scatter
Atmosphere.IRAY : Flag indicating the type of calculation for Rayleigh scattering
Atmosphere.ISCAT : Flat indicating what type of scattering calculation is required
Atmosphere.IMIE : Flag indicating whether to use Atmosphere.PHASE or Atmosphere.G1 and G2
Atmosphere.NDUST: Number of aerosol populations
Atmosphere.KEXT: Extinction cross section (cm2)
………………………………………………………….
Parameters and attributes
Methods
Scatter.write_xsc() : Write .xsc file
Scatter.calc_tau_dust(WAVEC,Layer) : Calculates the vertical opacity of each dust in each layer
Scatter.calc_tau_rayleighj(WAVEC,Layer) : Calculates the vertical opacity of Rayleigh scattering for giant planets
Scatter.read_xsc() : Reads .xsc file to fill the parameters and attributes of this class

## Slide 4
Third layer of code: Generating a forward model
Atmosphere
Measurement
Stellar
Surface
Spectroscopy
Scatter
CIA
Layer
Variables
subprofretg()
Model 1
Model 2
Model 3
……………
Atmosphere
Measurement
Stellar
Surface
Spectroscopy
Scatter
CIA
Layer
Variables
Calc_path()
Split atmosphere into layers and calculate parameters for each layer (stored in Layer).
Calculate atmospheric paths and set keywords
(stored in Path).
Layer
Path
CIRSrad
subspecret()
Model 1
Model 2
Model 3
……………
Measurement vector
Convolution

## Slide 5
Validation
Exoplanet emission with correlated-K defined in irregular grid (delv<0)
Classic Jupiter test (correlated-K)

## Slide 6
Things to discuss
Re-shaping the format of the input files? One file per Python class with little or no overlapping.
Example .inp file (but same for .set and others):
ISPACE
Measurement Class
ISCAT
Scatter Class
ILBL
Spectroscopy Class
NITER
Optimal Estimation Class
Best way to make it public? We can create a Python package that can be installed anywhere using:
pip install Nemesis
What next?
  Include more surface parameters and parameterisations:
    Surface.NMINERALS
    Surface.EMISSIVITY(NWAVE,NMINERALS)
    Will allow using Nemesis for surface studies too.
    Remove atmosphere?
  UV retrievals:
    Why not using .lta tables as in the infrared? I created a write_lta() function.
    Appears to work for O3 UV forward models in solar occultation.
  Include flags to include only certain things: ICIA, ISUR, IATM…

## Slide 7
Nemesis for UV
NOMAD UV retrievals in solar occultation